## Slide 1: KMDF
Power using KMDF

## Slide 2: Yesterday
DO_POWER_RUSH
  Power calculation
  Serialization between devices. Only one device transition to S0 with Power Rush.
WakeFromD0
  An overlook. Should be always True.

## Slide 3: IRP_MJ_POWER/IRP_MN_SET_POWER
Sent for both Sx and Dx state change
Parameters.Power.Type:
  SystemPowerState
    Parameters.Power.State is SYSTEM_POWER_STATE
    Must not fail.
  DevicePowerState
    Parameters.Power.State is DEVICE_POWER_STATE

## Slide 4: System IRP_MN_SET_POWER
PPO will set Completion routine
Call lower driver
System IRP for other drivers are FYI
On completion, complete first the system IRP
Then initiate a device IRP_MN_SET_POWER using the API: PoRequestPowerIRP

## Slide 5: IRP_MJ_POWER/IRP_MN_QUERY_POWER
Sent only when powering down
System will try to send whenever possible
  Will not send when pressing power button
  Will not send when battery runs out

## Slide 6: Power in KMDF driver
KMDF callbacks to communicate with driver PnP and Power events.
There is no SmplEvtIoPower callback
Framework handles many Power activities for us
By default, Framework delivers other I/O requests only if available and working (D0)
  Power managed queue (default). See with !wdfdevice

## Slide 7: During EvtDriverDeviceAdd
Call WdfDeviceInitSetPnpPowerEventCallbacks
  EvtDevicePrepareHardware
  EvtDeviceD0Entry
  EvtDeviceD0Exit
  EvtDeviceReleaseHardware
WdfDeviceSetPnpCapabilities, WdfDeviceSetPowerCapabilities
Wake: WdfDeviceInitSetPowerPolicyEventCallbacks
Functional driver: WdfFdoInitSetEventCallbacks

## Slide 8: Supporting idle power down
WdfDeviceAssignS0IdleSettings
WdfDeviceInitSetPowerPolicyEventCallbacks
  EvtDeviceArmWakeFromS0
  EvtDeviceDisarmWakeFromS0
  EvtDeviceWakeFromS0Triggered

## Slide 9: Supporting System Wake Up
WdfDeviceAssignSxWakeSettings
  Low power state that device can enter
  Whether user can control the idle settings.
  Device can wake

## Slide 10: I/O Queues
Group I/O requests to 2 categories
  Requests that requires D0 (Read, Write, etc.)
  Requests that not require D0 (some IO control, etc.)
Framework can create two queues, for each group.
  PowerManaged field in WDF_IO_QUEUE_CONFIG: WdfTrue or WdfFalse

## Slide 11: Sub-device power state
In Windows 8: Power Management Framework (PoFx)
F0, F1, F2, F3 states
Device runtime power management:
  Using D states
  Device Idle detection
Component level power management:
  Using F states
  Only while device is in D0 state

## Slide 12: PoFx functions
Registration
  PoFxRegisterDevice
  PoFxStartDevicePowerManagement
PoFxReportDevicePoweredOn

## Slide 13
[13]
Component Power Management
Optional (only available on Windows 8)
Component Power States
  ACPI (5.0) definition only for F0
  F0 = Fully powered on
  Power Policy Owner defines further states (F1,F2,..)
Component Power Events (Windows 8 only)
  Sent by Power Engine Plugin (PEP)
  Extending previous OS capabilities
Chapter 8: Power Management
...
...
...
F0
Notes: Chapter 5: Demand Paging Virtual Memory Architecture
© 2007 datronicsoft, Inc., Manila, Philippines
-13-

## Slide 14
[14]
Power Management Framework (PoFx)
Windows 8 Device Driver Interface (DDI)
Device power management
Device run time power management
  Using D-states
  Device idle detection
Component level power management
  Using F-States
  Side by side with device level power management
  Only while device is in D0 state
  Multiple components per device
Chapter 8: Power Management
Notes: Chapter 5: Demand Paging Virtual Memory Architecture
© 2007 datronicsoft, Inc., Manila, Philippines
-14-

## Slide 15
[15]
PoFx Functions
Registration with PoFx
  PoFxRegisterDevice()
  PoFxStartDevicePowerManagement()
PoFxReportDevicePoweredOn()
  Must be invoked by the driver
  Either after a system power transition to S0
  Or after DevicePowerRequiredCallback callback
PoFxSetDeviceIdleTimeout()
Activation/Idle reference counting
  PoFxActivateComponent()
  PoFxIdleComponent()
Chapter 8: Power Management
Notes: Chapter 5: Demand Paging Virtual Memory Architecture
© 2007 datronicsoft, Inc., Manila, Philippines
-15-

## Slide 16
[16]
PoFx Callbacks
Component power callbacks
  ComponentActiveConditionCallback
  ComponentIdleConditionCallback
  ComponentIdleStateCallback
Device power callbacks
  DevicePowerNotRequiredCallback
  DevicePowerRequiredCallback
Chapter 8: Power Management
Notes: Chapter 5: Demand Paging Virtual Memory Architecture
© 2007 datronicsoft, Inc., Manila, Philippines
-16-

## Slide 17
[17]
Chapter 8: Power Management
KMDF support for PoFx
KMDF supplies only a thin wrapper around PoFx
Device run-time power management (using D-states)
Component power management (using F-states)
  Limited WDF support (single component only)
KMDF source samples: SingleComp and MultiComp
Notes: Chapter 5: Demand Paging Virtual Memory Architecture
© 2007 datronicsoft, Inc., Manila, Philippines
-17-

## Slide 18: KMDF Power Device