## Slide 1: Power Management
August 2013, Intel Banglor

## Slide 2: whoami /all
whoami /fqdn
  uril@sela.co.il
  http://sela.co.il
  http://london.org.il
  Skype: uri-london
Material for the course:
  http://projects.london.org.il/pmgmt
  Lab solutions will be released as we progress

## Slide 3: Introduction
Power consumption scenarios:
  In general: desktop, servers in data center (energy is major cost).
  Mobile: Battery powered laptops
Windows computer can go to sleep or hibernate
  Attached device can power down
  Without loosing data!
Consideration:
  System Activity Level.
  System Battery Level.
  Current request to shutdown, sleep or hibernate
  User Actions such as pressing a button
  Control Panel Settings

## Slide 4: Scenarios
Customers demands computers to be available at all time, even when turned off!
OS, System, drivers, and devices must work together
Extending batter life
Minimal startup and shutdown delays
Near Silent (e.g. Media)

## Slide 5: Industry Initiatives
OnNow
Advanced Configuration and Power Interface (ACPI)
  Hardware level interface
Device Class Power Management Reference Specification
  For each device class (audio, network, etc.)
  http://www.acpi.info/

## Slide 6: Support for power management
To support power management, drivers must support PnP
  Power Management are associated with installing and removing devices
  PnP IRP’s
  Two levels: Individual devices and System
  Legacy: Fully on or fully off
  Drivers can put devices into intermediate steate

## Slide 7: Power Management Overview

## Slide 8: Power Manager
Power manager handles scenarios using IRPs
Considered a sub component of the IO manager
Po* routines: PoSetPowerState
WDF (specifically KMDF) makes power management easier.

## Slide 9: Power States
System Power States
  S0, S1, … , S5
Device Power States
  D0, D1, D2, D3
The smaller the number, the greater the power consumption (i.e. S0, D0 – fully on).
See Power Data in device manager

## Slide 10: Components
ACPI BIOS
ACPI Driver
  Loaded by the HAL
  Program components (e.g. WakeUp).
  For each device creates Filter DO
Power Manager
  Sends IRP_MJ_POWER
  Consider: Activity, Battery, Requests from app, User Action, Control Panel Policy
Drivers:
  Responds to Power Manager requests
  Manage their own device

## Slide 11: KMDF Refressher