## Slide 1: Connected Standby

## Slide 2: Overview
Power of mobile phone to Windows mobile
Windows 8.0 and 8.1
The main sleep state
  The default state when user press power button
  Appears to be sleep
Benefit:
  Instant resume. Less than 500 ms
  WiFi already connected
Screen is off

## Slide 3: Requirements
Low power core silicon (typically SoC).
Low power memory (DRAM)
Offload capable WiFi
Power efficient main board
Flash (SSD)
ACPI_S0_LOW_POWER_IDLE FADT
Passive cooling
Hibernate

## Slide 4: What is running
Device is connected (to Internet) to mobile and WiFi
  Device choose appropriate connection
Application gets information
Email is synched
Skype incoming calls
Application running in the background

## Slide 5: Power consumption
S3: 500 milliwatts to keep memory
Connected standby: due low power memory less than 150 milliwatts.
Enable sleep of 300 hours

## Slide 6: Application Activities
Create background task using WinRT
Lock screen interface
Audio notification

## Slide 7: Network
Responsible for connectivity while SoC remains on low power or idle mode
Protocol offload: ARP, NS, WiFi
WoL

## Slide 8: Functional
User press the power button
Windows immediately turn off display
Remote desktop session off
Suspend WRT (Windows Store) applications (PLM)
Maintenance Tasks
Desktop Activity Moderator
Resiliency phase (SoC go idle for 30 seconds)

## Slide 9: Hardware
Devices outside SoC
Network device goes to D2
On Host controllers: USB, I2C, GPIO,
Camera and other devices go to D3 cold
Powering down CPU DRIPS (Deepest Runtime Idle Platform State): S0ix, LP0
  Lowest power consumtion
  Memory refresh
  No CPU code

## Slide 10: Wake up
Every 30 seconds
On demand based on network
On demands based on battery, keyboard, usb