## Slide 1: ACPI Overview

## Slide 2: History
Advanced Power Management (APM)
  BIOS based
  CPU and device
  Uses device activity
  OS has no knowledge what APM does
  Each Bios Vendor has its own version
  Many implementations

## Slide 3: ACPI
Advanced Configuration and Power Interface
  Intel, Microsoft, Toshiba, HP, Phoenix
An Interface specification
  ACPI/OSPM replaces APM, and PnP Bios
Allow OS directed power management (OSPM)
Defines
  Hardware registers
  BIOS Interface
    Configuration tables (many)
    Executable function interface
    Motherboard device enumeration and configuration
  System and device power states
  ACPI Thermal model

## Slide 4: Global States and transition

## Slide 5: G and S states
G and S states describes the same thing: Global/System
G0 == S0
  System is working.
  “Away mode” is sub state of G0 where monitor is off and everything else is running
G1 == [S1, S2, S3, S4]
  S1: The processor caches are flushed. CPU stops executing instructions. Power to CPU and RAM maintained.
  S2: CPU powered off. Dirty cache is flushed to RAM
  S3: a.k.a. Sleep/Standby/Suspended. Power supply reduced.

## Slide 6: G and S states
G1
  S4: Hibernation. Main memory is saved to disk.
G2 == S5 (a.k.a. soft off)
  PSU still supplies power at minimum to the power button. Components like clock/keyboard/LAN can wake the system
G3
  Mechanical off. The system is safe for disassembly (real-time clock uses its own batter).

## Slide 7: Device States
D0: Fully on
D1, D2: Intermediate power states. Each device class has its own definition.
D3: Off. Unresponsive to its bus.
  D3 Hot: Auxiliary power. Can transition to higher state
  D3 Cold: No power provided

## Slide 8: Processor states
C0: operating
C1: Halt. Not executing instructions. Can return to C0 very fast.
C2: Save context, but wake up may be longer.
C3 (sleep): Maintain states. Doesn’t maintain cache.

## Slide 9: Performance states
Used by multi components devices. Each components has its own P state
P0 – fully on
P1 < P2 < P3 < … < Pn

## Slide 10: System

## Slide 11: Tables
DSDT
  Discrete System Descriptor Table
  AML (ACPI Machine Language)
  Compiled from ASL (ACPI Source Language)
  Definition blocks
FADT
  Fixed Address Descriptor Table
  Static structure (no code)
SRAT
  System Resource Affinity Table (Optional)
  Used by NUMA to define locality

## Slide 12: Scenarios
User hits the sleep key
  Hardware interrupt
  Change register in the Southbridge
  OS Notices it
  OS checks DSDT
  Goes to user space
  Policy implemented in user

## Slide 13: Components
ACPI Subsystem
  Consumes ACPI BIOS
  Interfaces with Hardware
Policy Manager (OSPM)
  Sets Policies
  User Interface
Device Drivers
  EC, SM Bus, CM Battery, Smart Battery

## Slide 14: System Overview

## Slide 15: Specification History
ACPI 1.0 – December 1996
ACPI 1.0a – July 1998
ACPI 2.0 – July 2000
ACPI 4.0a – April 2010
ACPI 5.0 – December 2011