## Slide 1: Power State

## Slide 2
Gobal Power State
  G0, G1, G2, G3
System Power State
  S0, S1, S2, S3, S4, S5
CPU Power State
  C0, C1, C2, C3
Bus Power State
  B0, B1, B2, B3
Device Power State
  D0, D1, D2, D3

## Slide 3: D0, D1, D2, D3
Power Consumption
Functionality
Restore time
Wakeup capabilities

## Slide 4: D0
Device is fully on and operational
Can access memory and IO ports
PoRequestPowerIrp – transit to other states

## Slide 5: D1 – D3
Power:
  D1 less than D0
  D2 less than D1
  D3hot – Power mostly detached.
  D3cold – presence cannot be detected. Power detached.
Context:
  D1 context stored by hardware
  D3hot context stored by driver (or re-initialize)

## Slide 6: Required support
D0 and D3 are required
Specifics for NDIS, SCSI, Video

## Slide 7: System State S0
Maximum Power
Individual devices may be powered down and up.

## Slide 8: S1, S2, S3, S4
Appears to be off
Memory preserved (in memory or disk)
S1 – no clock
S4 – no context (saved in disk)
Latency: S1 < 1s, S2 =~ 2s, S4 =
S4 is hibernate

## Slide 9
[9]
Chapter 8: Power Management
State transitions always have to go through S0
Enum name
ACPI State
PowerSystemShutdown
PowerSystemHibernate
PowerSystemSleeping3
PowerSystemSleeping2
PowerSystemSleeping1
PowerSystemWorking
S5
S4
S3
S2
S1
S0
WDM system power states
Notes: Chapter 5: Demand Paging Virtual Memory Architecture
© 2007 datronicsoft, Inc., Manila, Philippines
-9-

## Slide 10
[10]
Chapter 8: Power Management
No limits for state transitions
Implementation of D0 and D3 (other states optional)
D0 = Fully Powered on
D1 = Sleeping (almost on)
D2 = Sleeping (almost off)
D3 = Off
PowerDeviceD3
PowerDeviceD2
PowerDeviceD1
PowerDeviceD0
D3
D2
D1
D0
WDM device power states
Notes: Chapter 5: Demand Paging Virtual Memory Architecture
© 2007 datronicsoft, Inc., Manila, Philippines
-10-

## Slide 11: S5
Power off
Reboot required

## Slide 12: Power Policy
Two policies: AC and batteries
Select power source
Sends IRP_MJ_POWER